# USB Descriptors
All USB devices have a hierarchy of descriptors which describe to the host information such as what the device is, who makes it, what version of USB it supports, how many ways it can be configured, the number of endpoints and their types etc
The more common USB descriptors are
    - Device Descriptors
    - Configuration Descriptors
    - Interface Descriptors
    - Endpoint Descriptors
    - String Descriptors
USB devices can only have one device descriptor. The device descriptor includes information such as what USB revision the device complies to, the Product and Vendor IDs used to load the appropriate drivers and the number of possible configurations the device can have. The number of configurations indicate how many configuration descriptors branches are to follow.
The configuration descriptor specifies values such as the amount of power this particular configuration uses, if the device is self or bus powered and the number of interfaces it has. When a device is enumerated, the host reads the device descriptors and can make a decision of which configuration to enable. It can only enable one configuration at a time.
For example, It is possible to have a high power bus powered configuration and a self powered configuration. If the device is plugged into a host with a mains power supply, the device driver may choose to enable the high power bus powered configuration enabling the device to be powered without a connection to the mains, yet if it is connected to a laptop or personal organiser it could enable the 2nd configuration (self powered) requiring the user to plug your device into the power point.
The configuration settings are not limited to power differences. Each configuration could be powered in the same way and draw the same current, yet have different interface or endpoint combinations. However it should be noted that changing the configuration requires all activity on each endpoint to stop. While USB offers this flexibility, very few devices have more than 1 configuration.
The interface descriptor could be seen as a header or grouping of the endpoints into a functional group performing a single feature of the device. For example you could have a multi-function fax/scanner/printer device. Interface descriptor one could describe the endpoints of the fax function, Interface descriptor two the scanner function and Interface descriptor three the printer function. Unlike the configuration descriptor, there is no limitation as to having only one interface enabled at a time. A device could have 1 or many interface descriptors enabled at once.
Interface descriptors have a bInterfaceNumber field specifying the Interface number and a bAlternateSetting which allows an interface to change settings on the fly. For example we could have a device with two interfaces, interface one and interface two. Interface one has bInterfaceNumber set to zero indicating it is the first interface descriptor and a bAlternativeSetting of zero.
Interface two would have a bInterfaceNumber set to one indicating it is the second interface and a bAlternativeSetting of zero (default). We could then throw in another descriptor, also with a bInterfaceNumber set to one indicating it is the second interface, but this time setting the bAlternativeSetting to one, indicating this interface descriptor can be an alternative setting to that of the other interface descriptor two.
When this configuration is enabled, the first two interface descriptors with bAlternativeSettings equal to zero is used. However during operation the host can send a SetInterface request directed to that of Interface one with a alternative setting of one to enable the other interface descriptor.
This gives an advantage over having two configurations, in that we can be transmitting data over interface zero while we change the endpoint settings associated with interface one without effecting interface zero.
Each endpoint descriptor is used to specify the type of transfer, direction, polling interval and maximum packet size for each endpoint. Endpoint zero, the default control endpoint is always assumed to be a control endpoint and as such never has a descriptor.
# Composition of USB Descriptors
All descriptors are made up of a common format. The first byte specifies the length of the descriptor, while the second byte indicates the descriptor type. If the length of a descriptor is smaller than what the specification defines, then the host shall ignore it. However if the size is greater than expected the host will ignore the extra bytes and start looking for the next descriptor at the end of actual length returned.
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes
1	bDescriptionType	1	Constant	DescriptorType
2	...	n		Start of parameters for descriptor

# Device Descriptors
The device descriptor of a USB device represents the entire device. As a result a USB device can only have one device descriptor. It specifies some basic, yet important information about the device such as the supported USB version, maximum packet size, vendor and product IDs and the number of possible configurations the device can have. The format of the device descriptor is shown below.
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of the Descriptor in Bytes (18 bytes)
1	bDescriptorType	1	Constant	Device Descriptor (0x01)
2	bcdUSB	2	BCD	USB Specification Number which device complies too.
4	bDeviceClass	1	Class	Class Code (Assigned by USB Org) / If equal to Zero, each interface specifies it’s own class code / If equal to 0xFF, the class code is vendor specified. / Otherwise field is valid Class Code.
5	bDeviceSubClass	1	SubClass	Subclass Code (Assigned by USB Org)
6	bDeviceProtocol	1	Protocol	Protocol Code (Assigned by USB Org)
7	bMaxPacketSize	1	Number	Maximum Packet Size for Zero Endpoint. Valid Sizes are 8, 16, 32, 64
8	idVendor	2	ID	Vendor ID (Assigned by USB Org)
10	idProduct	2	ID	Product ID (Assigned by Manufacturer)
12	bcdDevice	2	BCD	Device Release Number
14	iManufacturer	1	Index	Index of Manufacturer String Descriptor
15	iProduct	1	Index	Index of Product String Descriptor
16	iSerialNumber	1	Index	Index of Serial Number String Descriptor
17	bNumConfigurations	1	Integer	Number of Possible Configurations

  - The bcdUSB field reports the highest version of USB the device supports. The value is in binary coded decimal with a format of 0xJJMN where JJ is the major version number, M is the minor version number and N is the sub minor version number. e.g. USB 2.0 is reported as 0x0200, USB 1.1 as 0x0110 and USB 1.0 as 0x0100.
  - The bDeviceClass, bDeviceSubClass and bDeviceProtocol are used by the operating system to find a class driver for your device. Typically only the bDeviceClass is set at the device level. Most class specifications choose to identify itself at the interface level and as a result set the bDeviceClass as 0x00. This allows for the one device to support multiple classes.
  - The bMaxPacketSize field reports the maximum packet size for endpoint zero. All devices must support endpoint zero.
  - The idVendor and idProduct are used by the operating system to find a driver for your device. The Vendor ID is assigned by the USB-IF.
  - The bcdDevice has the same format than the bcdUSB and is used to provide a device version number. This value is assigned by the developer.
  - Three string descriptors exist to provide details of the manufacturer, product and serial number. There is no requirement to have string descriptors. If no string descriptor is present, a index of zero should be used.
  - bNumConfigurations defines the number of configurations the device supports at its current speed.
# Configuration Descriptors
A USB device can have several different configurations although the majority of devices are simple and only have one. The configuration descriptor specifies how the device is powered, what the maximum power consumption is, the number of interfaces it has. Therefore it is possible to have two configurations, one for when the device is bus powered and another when it is mains powered. As this is a "header" to the Interface descriptors, its also feasible to have one configuration using a different transfer mode to that of another configuration.
Once all the configurations have been examined by the host, the host will send a SetConfiguration command with a non zero value which matches the bConfigurationValue of one of the configurations. This is used to select the desired configuration.
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes
1	bDescriptorType	1	Constant	Configuration Descriptor (0x02)
2	wTotalLength	2	Number	Total length in bytes of data returned
4	bNumInterfaces	1	Number	Number of Interfaces
5	bConfigurationValue	1	Number	Value to use as an argument to select this configuration
6	iConfiguration	1	Index	Index of String Descriptor describing this configuration
7	bmAttributes	1	Bitmap	D7 Reserved, set to 1. (USB 1.0 Bus Powered) / D6 Self Powered / D5 Remote Wakeup / D4..0 Reserved, set to 0.
8	bMaxPower	1	mA	Maximum Power Consumption in 2mA units

  - When the configuration descriptor is read, it returns the entire configuration hierarchy which includes all related interface and endpoint descriptors. The wTotalLength field reflects the number of bytes in the hierarchy.
  - bNumInterfaces specifies the number of interfaces present for this configuration.
  - bConfigurationValue is used by the SetConfiguration request to select this configuration.
  - iConfiguration is a index to a string descriptor describing the configuration in human readable form.
  - bmAttributes specify power parameters for the configuration. If a device is self powered, it sets D6. Bit D7 was used in USB 1.0 to indicate a bus powered device, but this is now done by bMaxPower. If a device uses any power from the bus, whether it be as a bus powered device or as a self powered device, it must report its power consumption in bMaxPower. Devices can also support remote wakeup which allows the device to wake up the host when the host is in suspend.
  - bMaxPower defines the maximum power the device will drain from the bus. This is in 2mA units, thus a maximum of approximately 500mA can be specified. The specification allows a high powered bus powered device to drain no more than 500mA from Vbus. If a device loses external power, then it must not drain more than indicated in bMaxPower. It should fail any operation it cannot perform without external power.
# Interface Descriptors
The interface descriptor could be seen as a header or grouping of the endpoints into a functional group performing a single feature of the device. The interface descriptor conforms to the following format,
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes (9 Bytes)
1	bDescriptorType	1	Constant	Interface Descriptor (0x04)
2	bInterfaceNumber	1	Number	Number of Interface
3	bAlternateSetting	1	Number	Value used to select alternative setting
4	bNumEndpoints	1	Number	Number of Endpoints used for this interface
5	bInterfaceClass	1	Class	Class Code (Assigned by USB Org)
6	bInterfaceSubClass	1	SubClass	Subclass Code (Assigned by USB Org)
7	bInterfaceProtocol	1	Protocol	Protocol Code (Assigned by USB Org)
8	iInterface	1	Index	Index of String Descriptor Describing this interface

  - bInterfaceNumber indicates the index of the interface descriptor. This should be zero based, and incremented once for each new interface descriptor.
  - bAlternativeSetting can be used to specify alternative interfaces. These alternative interfaces can be selected with the Set Interface request.
  - bNumEndpoints indicates the number of endpoints used by the interface. This value should exclude endpoint zero and is used to indicate the number of endpoint descriptors to follow.
  - bInterfaceClass, bInterfaceSubClass and bInterfaceProtocol can be used to specify supported classes (e.g. HID, communications, mass storage etc.) This allows many devices to use class drivers preventing the need to write specific drivers for your device.
  - iInterface allows for a string description of the interface.
# Endpoint Descriptors
Endpoint descriptors are used to describe endpoints other than endpoint zero. Endpoint zero is always assumed to be a control endpoint and is configured before any descriptors are even requested. The host will use the information returned from these descriptors to determine the bandwidth requirements of the bus.
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes (7 bytes)
1	bDescriptorType	1	Constant	Endpoint Descriptor (0x05)
2	bEndpointAddress	1	Endpoint	Endpoint Address Bits 0..3b Endpoint Number. Bits 4..6b Reserved. Set to Zero Bits 7 Direction 0 = Out, 1 = In (Ignored for Control Endpoints)
3	bmAttributes	1	Bitmap	Bits 0..1 Transfer Type / 00 = Control 01 = Isochronous 10 = Bulk 11 = Interrupt / Bits 2..7 are reserved. If Isochronous endpoint, Bits 3..2 = Synchronisation Type (Iso Mode) / 00 = No Synchonisation 01 = Asynchronous 10 = Adaptive 11 = Synchronous / Bits 5..4 = Usage Type (Iso Mode) / 00 = Data Endpoint 01 = Feedback Endpoint 10 = Explicit Feedback Data Endpoint 11 = Reserved
4	wMaxPacketSize	2	Number	Maximum Packet Size this endpoint is capable of sending or receiving
6	bInterval	1	Number	Interval for polling endpoint data transfers. Value in frame counts. Ignored for Bulk & Control Endpoints. Isochronous must equal 1 and field may range from 1 to 255 for interrupt endpoints.

  - bEndpointAddress indicates what endpoint this descriptor is describing.
  - bmAttributes specifies the transfer type. This can either be Control, Interrupt, Isochronous or Bulk Transfers. If an Isochronous endpoint is specified, additional attributes can be selected such as the Synchronisation and usage types.
  - wMaxPacketSize indicates the maximum payload size for this endpoint.
  - bInterval is used to specify the polling interval of certain transfers. The units are expressed in frames, thus this equates to either 1ms for low/full speed devices and 125us for high speed devices.
# String Descriptors
String descriptors provide human readable information and are optional. If they are not used, any string index fields of descriptors must be set to zero indicating there is no string descriptor available.
The strings are encoded in the Unicode format and products can be made to support multiple languages. String Index 0 should return a list of supported languages. A list of USB Language IDs can be found in Universal Serial Bus Language Identifiers (LANGIDs) version 1.0
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes
1	bDescriptorType	1	Constant	String Descriptor (0x03)
2	wLANGID[0]	2	number	Supported Language Code Zero (e.g. 0x0409 English - United States)
4	wLANGID[1]	2	number	Supported Language Code One (e.g. 0x0c09 English - Australian)
n	wLANGID[x]	2	number	Supported Language Code x (e.g. 0x0407 German - Standard)

The above String Descriptor shows the format of String Descriptor Zero. The host should read this descriptor to determine what languages are available. If a language is supported, it can then be referenced by sending the language ID in the wIndex field of a Get Descriptor(String) request.
All subsequent strings take on the format below,
Offset	Field	Size	Value	Description
0	bLength	1	Number	Size of Descriptor in Bytes
1	bDescriptorType	1	Constant	String Descriptor (0x03)
2	bString	n	Unicode	Unicode Encoded String

# The Setup Packet
Every USB device must respond to setup packets on the default pipe. The setup packets are used for detection and configuration of the device and carry out common functions such as setting the USB device’s address, requesting a device descriptor or checking the status of a endpoint.
A USB compliant Host expects all requests to be processed within a maximum period of 5 seconds. It also specifies stricter timing for specific requests :
  - Standard Device requests without a data stage must be completed in 50ms.
  - Standard Device requests with a data stage must start to return data 500ms after the request.
    - Each data packet must be sent within 500ms of the successful transmission of the previous packet.
    - The status stage must complete within 50ms after the transmission of the last data packet.
  - The SetAddress command (which contains a data phase) must process the command and return status within 50ms. The device then has 2ms to change address before the next request is sent.
These timeout periods are quite acceptable for even the slowest of devices, but can be a restriction during debugging. 50mS doesn't provide for many debugging characters to be sent at 9600bps on an asynchronous serial port or for a In Circuit Debugger/Emulator to single step or to break execution to examine the internal Registers. As a result, USB requires some different debugging methods to that of other microcontroller projects.
  Casually reading through the XP DDK, one may note the Host Controller Driver now has a USBUSER_OP_SEND_ONE_PACKET command which is commented to read "This API is used to implement the 'single step' USB transaction development tool." While such a tool has not been released yet, we can only hope to see one soon.
Each request starts with a 8 byte long Setup Packet which has the following format,
Offset	Field	Size	Value	Description
0	bmRequestType	1	Bit-Map	D7 Data Phase Transfer Direction 0 = Host to Device 1 = Device to Host D6..5 Type 0 = Standard 1 = Class 2 = Vendor 3 = Reserved D4..0 Recipient 0 = Device 1 = Interface 2 = Endpoint 3 = Other 4..31 = Reserved
1	bRequest	1	Value	Request
2	wValue	2	Value	Value
4	wIndex	2	Index or Offset	Index
6	wLength	2	Count	Number of bytes to transfer if there is a data phase

The bmRequestType field will determine the direction of the request, type of request and designated recipient. The bRequest field determines the request being made. The bmRequestType is normally parsed and execution is branched to a number of handlers such as a Standard Device request handler, a Standard Interface request handler, a Standard Endpoint request handler, a Class Device request handler etc. How you parse the setup packet is entirely up to your preference. Others may choose to parse the bRequest first and then determine the type and recipient based on each request.
Standard requests are common to all USB device's and are detailed in the next coming pages. Class requests are common to classes of drivers. For example, all device conforming to the HID class will have a common set of class specific requests. These will differ to a device conforming to the communications class and differ again to that of a device conforming to the mass storage class.
And last of all are the vendor defined requests. These are requests which you as the USB device designer can assign. These are normally different from device to device, but this is all up to your implementation and imagination.
A common request can be directed to different recipients and based on the recipient perform different functions. A GetStatus Standard request for example, can be directed at the device, interface or endpoint. When directed to a device it returns flags indicating the status of remote wakeup and if the device is self powered. However if the same request is directed at the interface it always returns zero, or should it be directed at an endpoint will return the halt flag for the endpoint.
The wValue and wIndex fields allow parameters to be passed with the request. wLength is used the specify the number of bytes to be transferred should there be a data phase.
# Standard Requests
Section 9.4 of the USB specification details the "Standard Device" requests required to be implemented for every USB device. The standard provides a single table grouping items by request. Considering most firmware will parse the setup packet by recipient we will opt to break up the requests based by recipient for easier examination and implementation.
# Standard Device Requests
There are currently eight Standard Device requests, all of which are detailed in the table below.
bmRequestType	bRequest	wValue	wIndex	wLength	Data
1000 0000b	GET_STATUS (0x00)	Zero	Zero	Two	Device Status
0000 0000b	CLEAR_FEATURE (0x01)	Feature Selector	Zero	Zero	None
0000 0000b	SET_FEATURE (0x03)	Feature Selector	Zero	Zero	None
0000 0000b	SET_ADDRESS (0x05)	Device Address	Zero	Zero	None
1000 0000b	GET_DESCRIPTOR (0x06)	Descriptor Type & Index	Zero or Language ID	Descriptor Length	Descriptor
0000 0000b	SET_DESCRIPTOR (0x07)	Descriptor Type & Index	Zero or Language ID	Descriptor Length	Descriptor
1000 0000b	GET_CONFIGURATION (0x08)	Zero	Zero	1	Configuration Value
0000 0000b	SET_CONFIGURATION (0x09)	Configuration Value	Zero	Zero	None

  - The Get Status request directed at the device will return two bytes during the data stage with the following format,
D15	D14	D13	D12	D11	D10	D9	D8	D7	D6	D5	D4	D3	D2	D1	D0
Reserved														Remote Wakeup	Self Powered

  If D0 is set, then this indicates the device is self powered. If clear, the device is bus powered. If D1 is set, the device has remote wakeup enabled and can wake the host up during suspend. The remote wakeup bit can be by the SetFeature and ClearFeature requests with a feature selector of DEVICE_REMOTE_WAKEUP (0x01)
  - Clear Feature and Set Feature requests can be used to set boolean features. When the designated recipient is the device, the only two feature selectors available are DEVICE_REMOTE_WAKEUP and TEST_MODE. Test mode allows the device to exhibit various conditions. These are further documented in the USB Specification Revision 2.0.
  - Set Address is used during enumeration to assign a unique address to the USB device. The address is specified in wValue and can only be a maximum of 127. This request is unique in that the device does not set its address until after the completion of the status stage. (See Control Transfers.) All other requests must complete before the status stage.
  - Set Descriptor/Get Descriptor is used to return the specified descriptor in wValue. A request for the configuration descriptor will return the device descriptor and all interface and endpoint descriptors in the one request.
    - Endpoint Descriptors cannot be accessed directly by a GetDescriptor/SetDescriptor Request.
    - Interface Descriptors cannot be accessed directly by a GetDescriptor/SetDescriptor Request.
    - String Descriptors include a Language ID in wIndex to allow for multiple language support.
  - Get Configuration/Set Configuration is used to request or set the current device configuration. In the case of a Get Configuration request, a byte will be returned during the data stage indicating the devices status. A zero value means the device is not configured and a non-zero value indicates the device is configured. Set Configuration is used to enable a device. It should contain the value of bConfigurationValue of the desired configuration descriptor in the lower byte of wValue to select which configuration to enable.
# Standard Interface Requests
The specification currently defines five Standard Interface requests which are detailed in the table below. Interestingly enough, only two requests do anything intelligible.

bmRequestType	bRequest	wValue	wIndex	wLength	Data
1000 0001b	GET_STATUS (0x00)	Zero	Interface	Two	Interface Status
0000 0001b	CLEAR_FEATURE (0x01)	Feature Selector	Interface	Zero	None
0000 0001b	SET_FEATURE (0x03)	Feature Selector	Interface	Zero	None
1000 0001b	GET_INTERFACE (0x0A)	Zero	Interface	One	Alternate Interface
0000 0001b	SET_INTERFACE (0x11)	Alternative Setting	Interface	Zero	None

wIndex is normally used to specify the referring interface for requests directed at the interface. Its format is shown below.
D15	D14	D13	D12	D11	D10	D9	D8	D7	D6	D5	D4	D3	D2	D1	D0
Reserved								Interface Number

- Get Status is used to return the status of the interface. Such a request to the interface should return two bytes of 0x00, 0x00. (Both bytes are reserved for future use)
- Clear Feature and Set Feature requests can be used to set boolean features. When the designated recipient is the interface, the current USB Specification Revision 2 specifies no interface features.
- Get Interface and Set Interface set the Alternative Interface setting which is described in more detail under the Interface Descriptor.
# Standard Endpoint Requests
Standard Endpoint requests come in the four varieties listed below.
bmRequestType	bRequest	wValue	Windex	wLength	Data
1000 0010b	GET_STATUS (0x00)	Zero	Endpoint	Two	Endpoint Status
0000 0010b	CLEAR_FEATURE (0x01)	Feature Selector	Endpoint	Zero	None
0000 0010b	SET_FEATURE (0x03)	Feature Selector	Endpoint	Zero	None
1000 0010b	SYNCH_FRAME (0x12)	Zero	Endpoint	Two	FrameNumber

  - The wIndex field is normally used to specify the referring endpoint and direction for requests directed to an endpoint. Its format is shown below.
D15	D14	D13	D12	D11	D10	D9	D8	D7	D6	D5	D4	D3	D2	D1	D0
Reserved								Dir	Reserved			Endpoint Number

  - Get Status returns two bytes indicating the status (Halted/Stalled) of a endpoint. The format of the two bytes returned is illustrated below.
D15	D14	D13	D12	D11	D10	D9	D8	D7	D6	D5	D4	D3	D2	D1	D0
Reserved															Halt

  - Clear Feature and Set Feature are used to set Endpoint Features. The standard currently defines one endpoint feature selector, ENDPOINT_HALT (0x00) which allows the host to stall and clear an endpoint. Only endpoints other than the default endpoint are recommended to have this functionality.
  - A Synch Frame request is used to report an endpoint synchronisation frame.